## Slide 1
Péter Györke http://www.mit.bme.hu/~gyorke/
gyorke@mit.bme.hu
Budapest University of Technology and Economics (BME)
Department of Measurement and Information Systems (MIT)
The slides of the latest lecture will be on the course page. (https://www.mit.bme.hu/eng/oktatas/targyak/vimiab00) These slides are under copyright.
Operating Systems – Memory management

## Slide 2: The main blocks of the OS and the kernel (recap)
Hardware devices
System libraries
System processes
User processes
Non-protected
(user)
Protected
(system)
Device managers
Loader
Scheduler
IT handler
I/O operations
Systemcall interface
Memory manager
Communications
Process management

## Slide 3: Data structures of the tasks (recap)
Activities performed by programs
  Tasks have state and life-cycle
  Tasks have own and administrative data structures
Program data (in the task’s memory range)
  Code
  Static allocated data
  Stack: temporary storage, e.g. for function calls
  Heap: runtime (dynamic) allocated memory space
Administrative data (managed by the kernel)
  Task (process, thread) descriptor
  Unique ID (PID, TID)
  State
  Context of the task: the descriptor of the execution state
    Program counter, CPU registers
    Scheduling information
    Memory management state (MMU state)
  Owner and permissions
  I/O state information
Stack
Free memory
Heap
Static data
Code
PID
State
Context
Permissions
I/O state
…

## Slide 4: Separation of the tasks (abstract virtual machine concept)
The ideal scenario: every task runs independent of each other
  No effects on other tasks
  It seems they running on a separate machine (resources)
In the reality: not enough resources for each task
  They have to share the resources (CPU, memory, etc.)
  Goal: the task (and the user) don’t notice this
  The kernel provides an abstract virtual machine for the tasks (virtual CPU and memory)
  A typical multi-programmed system
    M processor (1<= M <= 8), N task (N > 10-100)
    More task than processor (N >> M)
    N abstract virtual machines have to be assigned to the physical resources
    In a way that the tasks don’t the existence of other tasks, but still sharing the common resources
Complex activities require more than one task: this makes the situation more complex
  Communication (IPC) and cooperation schemas have to be provided

## Slide 5: Memory management
Storing and managing task’s data structures in the RAM
  Code and static data are loaded from the HDD
  Dynamic data: heap and stack
The kernel allocates some memory for its own data structures
  Code and static data are loaded at the system boot
Typically there isn’t enough physical memory
  Multiprogrammed systems: multiple tasks are loaded at the same time  using memory
  The OS try to provide memory for every task
   the OS virtually increase the size of the physical memory: virtual memory
The data structures of the tasks and the kernel should be protected
  The physical memory sections are separated to ensure safe operation of the tasks (others can’t corrupt their data)
  Memory management provides the separation usually with HW support
  The kernel manages the occurred errors: general protection fault, illegal addressing  the faulty task will be stopped
Supporting communication
  Tasks may communicate with each other, or with the kernel
Increasing efficiency
  Shared memory ranges (e.g. code), avoiding unnecessary allocations

## Slide 6: Typical task memory usage
The code and data are in the same memory
  Neumann architecture
At the start the tasks don’t need all of their code and data
Dynamic allocation during runtime
  The tasks don’t mind the size of the physical memory
  They can dynamically allocate a larger memory section
  The allocated memory often not used entirely
There are locality properties
  Temporal locality: repeated operations on the same data
  Spatial locality: operations on data near each other
  Algorithmic locality: patters in the operation
There can be never used code and data
  The execution of the program code can different, influenced by external circumstances
  Many functions are rarely used (exceptions, rare operations)
The tasks may share some of their code and data

## Slide 7: Virtual memory management
Based on the typical usage and on the abstract virtual machine concept…
The current OSs using virtual memory management
  It provides a separated, contiguous virtual memory range
  Manages the association between the virtual and physical memory sections
  Providing memory for more tasks at the same time
  Allocating only the necessary memory range for the tasks
  It is possible to fulfill higher demands than the physical memory
  The tasks may have shared ranges (read-only)
  In the meantime the kernel provides separation and protection
The basic methods of MM
  Association of virtual and physical addresses: address translation
  Separation of the tasks memory range with HW support: paging
  Extending the (fast) physical memory size with (slow) HDD: swap

## Slide 8: Address translation and paging
The tasks of the Memory Management Unit (MMU)
  Address translation: from CPU address to physical RAM and I/O addresses
Address translation in virtual MM
  The tasks reach the whole CPU memory range
    This is the virtual range
      E.g.: x86-64: 248 = 256 terabyte
    The physical memory is only a fragment of this
      It may addressed with the physical memory address range
    If there are no sufficient physical memory, the rest will be stored on the HDD
The memory organized in pages
  The virtual range is divided into equal size pages
  The physical memory is also divided into same size frames
  The pages stored on the HDD in blocks
  Page table: association between physical frames, virtual pages and HDD blocks
    Valid (=1, it’s in the physical memory)
    Dirty (=0, the data is the same as the stored version on the HDD)
    Accessed (=1, recently used page)
  Translation Lookaside Buffer (TLB): accelerating the address translation
HDD
Physical memory
Virtual memory
Address translation

## Slide 9: Address translation and page table
The common hardware uses hierarchical page table
  The page table is also divided into pages
  Relatively fast
  Not stored entirely in the memory
  On 64-bit systems it can be tree (4-6 levels)
  It is used by ARM and x86 architectures also
The steps of address translation
  Subdividing addresses
    Page number index
    Offset
  The physical frame is identified by the index
  The offset is added to the index
Address (task) separation
  Usually separate page tables for tasks
    The page table is part of the tasks context
Valid?
1 | 43 | Y
2 | 43 | N
3 | - | N
4 | - | N
5 | 57 | Y
6 | - | N
7 | 36 | N
8 |  | 
page num. | offset
1 | 489
start address | offset
43 | 489
Virt. address
Phy. address
Single level page table

## Slide 10: Swap (or aka pagefile)
It is used to extend the capacity of the phyisical memory
  It is divivided into blocks
  Code and date also can be stored in the blocks
  CPU cannot access these data directly
    First it has to loaded into the physical memory
  Significantly slower than physical memory
Swapping
  If the stored data is requested by the CPU, it has to loaded back into the RAM
  If we need more space in the RAM, some frames have to be moved to the swap
Initial implementation of swapping
  The developement started before the paging is used
  The whole task’s memory range was written to the HDD, to free physical memory
  This caused the fragmentation of the RAM and the swap space
    Variable size „holes” appeared in the ranges, hard to fill these without gaps
    They try to manage this by dynamically reordering the memory spaces

## Slide 11: Virtual memory management
Based on paging and abstract virtual machine concept
  The memory range of tasks are divided into pages (no/less fragmentation)
  The pages are stored in the RAM or in the swap
  The HW MMU is configured to support this behavior
  The MMU interrupts has to be managed
During task execution
  The TLB and MMU translates the virtual addresses to physical addresses
  The protection of the pages is done by the MMU HW
    IT is generated, when an error occurs
Managing ITs by MMU
  Protection fault: the running task try to access and address outside its range
    E.g.: bad pointer
    The operation of this task should be terminated
  Page fault: the requested page is not in the physical memory
    Before the task continue its operation, the page has to be loaded back to RAM

## Slide 12: Managing page faults
The requested page is not valid (valid=0)
  A page fault IT is generated by the MMU, the kernel’s IT handler starts to run
  It determines the source of the requested page
    It is on the HDD swap space
    Fill-on-demand
      Zero-fill: e.g. dynamically allocated memory
      Fill-from-text: for loading code or static data from the HDD
  It starts loading the data to an empty physical frame
    If there are no free frames, one of them has to swapped
    If there is a free frame, the starting address of the frame is stored into the page table
    This I/O op. may be long, so the task is entered into waiting state
  The kernel returns from the IT handler (changes to another task)
When the page load is done
  The page table entry will be set to valid (valid=1)
  The task will be ready-to-run
When the task gets in running state
  The operation is continues from the instruction which caused the page fault

## Slide 13: Further tasks of the kernel’s memory manager
Providing free frames in the physical memory
  It is a basic condition to solve page faults, but is also required for new allocations
  This should be done in advance, when the system is lightly loaded freeing unused frames
  If there are no free frames and a page fault happens  page swap
  There are multiple swapping strategies (see later)
Administering
  The pages of virtual memory – page table
  The frames of the physical memory – page frame data
  The swap space on the HDD – disc block descriptor and swap map
Further tasks
  Updating the page table with the MMU
  Storing frames to the HDD which are cannot fit into the RAM
  Loading requested pages from HDD
  If required whole tasks may be swapped to the HDD

## Slide 14: The data structures of virtual memory management
Page frame data (pfdata) entry (kernel)
  Every frame has one entry, indexed by the starting address of the frame
  State: free, used, under DMA op., etc.
  Reference counter: how many task uses this frame
Kernels page table entry (part of task’s context)
  There fields used by the MMU HW
    Index of the page
    Frame identifier (where is (was) the page in the RAM)
    Valid bit: =1 if the page is in the RAM
    Dirty bit: =1 if the page is written since it is in the RAM
    Accessed bit: =1 if the page is „recently” accessed
    Read-only bit
  There are fields which not managed by the MMU (HW dependent)
    Page state: in RAM, on disk, fill-on-demand
    Task ID, copy-on-write bit, permissions, etc.
Disk block descriptor (kernel)
  The disk ID: which file on which disk
  Block index
  Type: swap, fill-on-demand

## Slide 15: References between date structures and address translation
page num. | offset
2 | 489
start address | offset
43 | 489
Virt. address
Phy. address
Page table and disc block desc.
 | frame | valid |  | device | idx
1 | 43 | Y |  | sda1 | 5
2 | 43 | N |  | swap | 3
3 | - | N |  | sda1 | 6
4 | - | N |  | ZF | 
5 | 57 | N |  | swap | 36
6 | 36 | N |  | swap | 13
7 |  | N |  |  | 
8 |  |  |  |  | 
addr. | state | acc | dirty
36 | free | 0 | 0
43 | used | 1 | 0
57 | used | 2 | 1
Page frame data

## Slide 16: Performance boosting techniques: fill-on-demand
The tasks are allocating memory dynamically (e.g. malloc())
  After the allocation the memory is uninitialized, the contents is undefined
  Therefore a physical frame is not allocated, only a page table entry is generated
Operation of a fill-on-demand entry
  The kernel don’t allocate a physical frame during malloc()
  The new page table entry will be marked with fill-on-demand flag: fill-on-demand/zero-fill (ZF)
  When the task tries to access the data first time
    The MMU generates a page fault IT
    The kernel’s IT handler detects that a new frame has to be allocated from the free frames
    Based on the flag, the frame will be filled with zeros or data from the disc (fill-from-text)
    After the IT returns, the task can access the data
With this technique the tasks can allocate memory efficiently
  Only allocating resources when they are actually needed

## Slide 17: Performance boosting techniques: copy-on-write (COW)
The number of used physical memory frames may be decreased with page sharing
  More than one task can use the same frames
  No problem when there are just read operations
  In the case of writing, the frame will be duplicated and the writer task gets the new instance
Memory management of the processes created by fork() system call
  The fork() in UNIX systems is used to create a new process by duplicating the memory range of the caller task
    The new process (child) is the exact copy of the parent
  The child process inherits the parents page table entries, no new physical frame is allocated
    The reference counter is increased in the page frame data
    The read-only (RO) and copy-on-write (COW) flags are set
  The two process are sharing the same frames and swap space
  When one of the tasks tries to write one on the frames
    Due to the RO bit, a HW IT is generated
    The kernel’s IT handler detects the RO and COW bits, so new frame will be allocated, and the data is copied
    The RO and COW bits are cleared on both frames
    Returns from the IT and the task can continue its write operation
  Very efficient way to create new processes
COW is a common technique in UNIX and Windows also

## Slide 18: Which pages should be in the physical memory?
A high page fault frequency (PPF) is disadvantageous
  Managing page faults usually introduce
    A high number of ITs  high number of context changes
    Additional I/O operations
  The tasks execution is interrupted, waiting state, re-scheduling
    A CPU intensive task may become I/O intensive, however the task don’t execute any I/O operations
  The overhead is getting higher  system performance degradation
    Thrashing: high PPF, severe performance degradation
    Managing a page fault may introduce another page fault, more and more I/O operations, CPU utilization decreases
    It may be managed by a medium-term scheduler, constraining the number of tasks
If a task has many pages in the RAM
  The number of page faults will be lower for this task
  The other task will won’t get enough physical memory
If a task has few frames in the RAM
  A high number of tasks may execute simultaneously
  Each task will generate a high number of page faults  slower operation

## Slide 19: The emergence of trashing

## Slide 20: Paging strategies
Demand paging
  Only runs when a page fault occurs, loads only the requested page
  Simple, only the requested pages will be loaded to RAM
  Every time a new page is requested, a PF will be generated
    This can significantly slow tasks down (CPU intensive task will become I/O intensive)
    E.g. iterated over a large data structure
    Every PF will enter the task into waiting state  high number of context changes, inefficient I/O operations
Anticipatory paging
  It’s try to figure out which pages will be requested
    It is based on the locality properties of the tasks
    And the tasks PF rate, higher PFF  more pages should be loaded to RAM
  A good prediction will significantly lower the number of page faults
  A „less good” prediction may load pages which are unnecessarily using the RAM at the moment
    If there are enough RAM, it isn’t a serious problem
  Observing the global PFF, the number of active tasks can be determined
    In order to avoid trashing, a number of active tasks should be decreased

## Slide 21: Page replacement algorithms – introduction
A page has to be loaded, but there are no free frames
  A used frame has to be picked, which will be moved to the swap space and mark as free
The picking based on
  Accessed bit: Is it used „recently”?
  Dirty bit: Is the contents modified?
  The allocation time of the frame
  The latest access time of the frame
  Reference counter: how many task uses this frame?
The properties of page replacement algorithms
  Ideal solution: seeing the future
    It is similar to the estimation of the CPU burst of a task
    In practice, the prediction is based on the behavior in the past
  The frame to swap may be chosen from the actual task’s (local) range or from the global range
  Algorithms (details on following slides)
    FIFO: the page loaded first will be replaced first
    Second chance (SC): oldest and not accessed page
    Least Recently Used (LRU): the oldest accessed page
    Least Frequently Used (LFU): the most rarely used page
    Not Recently Used (NRU): Non accessed and non modified page

## Slide 22: FIFO page replacement and Bélády’s anomaly
Simple, low overhead, backward looking algorithm
When a page is associated with a frame (loaded into the RAM) it will be queued in a FIFO queue
If a free frame is needed
  From the front of the queue a page table entry is picked
  The associated frame will be written to the HDD
  The frame will be freed and the new allocation can be made
What happens if we increase the available frame count?
  It is expected that PF rate will decrease
  In practice this isn’t always the case: from time to time the PF rate will increase when the available frame count is higher
  This is called the Bélády’s anomaly (László Bélády, IBM virtual memory management)
Evaluating FIFO algorithm
  Simple, simple implementation, low overhead
  The estimation of the future demand is poor
  It cannot differentiate between modified and unchanged pages, it may replace unchanged pages  unnecessary disk operations

## Slide 23: Example of Bélády’s anomaly
Page requests | FIFO (3 fr) |  |  |  |  | FIFO (4 fr) |  |  |  | 
3 |  | 3 |  |  |  | 3 |  |  |  | 
2 |  | 2 | 3 |  |  | 2 | 3 |  |  | 
1 |  | 1 | 2 | 3 |  | 1 | 2 | 3 |  | 
0 |  | 0 | 1 | 2 |  | 0 | 1 | 2 | 3 | 
3 |  | 3 | 0 | 1 |  | 0 | 1 | 2 | 3 | 
2 |  | 2 | 3 | 0 |  | 0 | 1 | 2 | 3 | 
4 |  | 4 | 2 | 3 |  | 4 | 0 | 1 | 2 | 
3 |  | 4 | 2 | 3 |  | 3 | 4 | 0 | 1 | 
2 |  | 4 | 2 | 3 |  | 2 | 3 | 4 | 0 | 
1 |  | 1 | 4 | 2 |  | 1 | 2 | 3 | 4 | 
0 |  | 0 | 1 | 4 |  | 0 | 1 | 2 | 3 | 
4 |  | 0 | 1 | 4 |  | 4 | 0 | 1 | 2 | 
time
Number of PF when the FIFO size is 3: 9
Number of PF when the FIFO size is 4: 10

## Slide 24: Second chance (SC) page replacement algorithm
SC also uses FIFO data structure
  When a page is associated with a frame it will be queued in a FIFO queue
From the front of the queue the page table entry is picked
  If (accessed_bit == 1) //MMU sets this bit
    accessed_bit = 0;
    The page table entry is moved back to the back of the queue
  Else
    The page is not used recently, so this will be replaced
Evaluating SC algorithm
  Simple, simple implementation, low overhead
  The future demand estimation is better than pure FIFO
    The accessed bit is showing the recent usage of a page
  It still cannot differentiate between modified and unchanged pages, it may replace unchanged pages  unnecessary disk operations

## Slide 25: Least Recently Used (LRU) page replacement algorithm
The pages are ordered in a queue based on their last access time
  There are multiple implementations based on the MMU HW
  The page table entries are stored in an ordered chained list
  There are also a reference counter for each page
  The page with the smallest value will be replaced
Evaluating LRU algorithm
  Complex, high overhead, is should be implemented only with HW support
  It gives a very good estimation of the future usage of the pages
  Problem: a new page can be replaced with high priority
  It still cannot differentiate between modified and unchanged pages, it may replace unchanged pages  unnecessary disk operations

## Slide 26: Least Frequently Used (LFU) page replacement algorithm
The simplified version of the LRU alg.
  It can be implemented without HW support
  The OS periodically checks that a page is used or not, if used a counter will be incremented
    This not happens with every memory operation like in LRU
Evaluating LFU algorithm
  Medium overhead
  It’s a rather good estimation of the future uses of pages
  Problem: a new page can be replaced with high priority
  The counter can overflow (aging can handle this)
  It still cannot differentiate between modified and unchanged pages, it may replace unchanged pages  unnecessary disk operations

## Slide 27: Not Recently Used (NRU) page replacement algorithm
The refined version of the SC alg.
  Beside the accessed bit, the dirty bit is also taken into account
  With this two bit, a „priority” is assigned to each page
    acc=0, dirty = 0  pri = 0
    acc=0, dirty = 1  pri = 1
    acc=1, dirty = 0  pri = 2
    acc=1, dirty = 1  pri = 3
  If a frame is needed, the one with the smallest priority will be chosen
Evaluating NRU algorithm
  Low overhead, good utilization of the HW bits
  Better estimation than SC
  It can differentiate between the modified and unchanged pages

## Slide 28: Page locking
Multiple algorithms suffer from the same problem: the newly loaded pages
  The newly loaded pages don’t have „past”, ( e.g.: no counter values)
  Therefore the future is hard to estimate
  There is high chance this pages will be replaced
Pages under I/O operation cannot be replaced
  I/O operations using physical addresses
  With DMA, these operation can be done without the CPU (in the background, simultaneously)
Page locking can solve these problems
  A special page lock bit is used
  The locked pages cannot be replaced
  The locking is maintained until the end of the I/O operations
  With LRU and LFU algorithms the page is usually locked until it’s first access

## Slide 29: Providing free frames: page daemon task
The page replacement usually happens at the „wrong” time
  The replacement happens when there are no free frames, so it must happen
  The free frames can be run out because the high system load  this isn’t an ideal time for page replacement (context change, I/O, etc.)
  It would be better to do this when the system load is low
Page daemon task (kswapd, Working Set Manager)
  It runs periodically by the kernel
  It tries to maintain the number of free frames between two thresholds
    If the number drops below a minimum value, then additional frames will be freed up (e.g.: with NRU alg.), until the maximum value is reached
  It may maintain the data structures for page replacement algorithms
    Resetting accessed bit
    Aging the counters
  This kernel process may also perform the page replacement also
    Despite the operation of this task, if the free frames still run out, the page replacement should be performed ASAP

## Slide 30: Summary
The concept of abstract virtual machine in multiprogrammed systems
  The tasks get their own virtual memory range
The tasks of the kernel’s memory manager
  Translating between virtual and physical addresses
  Usually there are not enough physical memory  swapping
  The memory is organized into pages/frames/blocks to avoid fragmentation
  The virtual pages are assigned to RAM frames or disk blocks
  The memory ranges of different tasks are protected
  To improve efficiency some ranges can be shared
Address translation
  Works with HW support (MMU, TLB)
  If the HW generates page fault IT, the SW page management steps in
The kernel manages page faults (PF), it tries to avoid thrashing
  There are different page replacement algorithms to free physical frames
  It tries to decrease the PF rate with future page demand allocation